## Slide 1: Machine Learning for Uncertainty Quantification (UQ): Trusting the Black Box
Defense and Aerospace Test and Analysis Workshop (DATAWorks) 2022
April 27th, 2022
James Warner, Geoffrey Bomarito, Patrick Leser, Paul Leser
NASA Langley Research Center
Hampton, Virginia

## Slide 2: Motivation: Modeling & Simulation
…
Model
Inputs
Outputs

## Slide 3: Motivation: Modeling & Simulation
Model
Inputs
Outputs
Deformation, Stress, Strain
Max contact force
Atmospheric conditions
Mass properties
Landing location
Impact velocity
Lunar regolith properties
Applied load
Material properties
Spacesuit Impact Model
Trajectory Simulation
Mechanical Testing Simulation
Notes: EDL – D205
Aero – D308

## Slide 4: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Repeated Evaluations
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation

## Slide 5: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Expected landing location
Statistical estimators
Repeated Evaluations
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation

## Slide 6: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Expected landing location
95% confidence landing ellipse
95% Probability
Confidence/credible intervals
Repeated Evaluations
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation

## Slide 7: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Expected landing location
95% confidence landing ellipse
Probability of failure
Percentiles & Rare event probabilities
Repeated Evaluations
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation
Notes: Mention inverse problem

## Slide 8: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Repeated Evaluations
Measurements,
Inverse problem
Estimated input probability density functions (PDFs),
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Expected landing location
95% confidence landing ellipse
Probability of failure
Calibrated material parameter PDFs
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation
Notes: Mention inverse problem

## Slide 9: UQ for Modeling & Simulation
Inputs
Outputs
Spacesuit Impact Model
Max contact force
Model
Number of Model Evaluations O(103-106)
Computation Time: O(mins-hours)
Computation Time: O(hours-days)
UQ with high-fidelity, physics-based models can be computationally intractable
Impact velocity
Lunar regolith properties
Mechanical Testing Simulation
Deformation, Stress, Strain
Applied load
Material properties
Computation Time: O(sec-mins)
Atmospheric conditions
Mass properties
Landing location
Trajectory Simulation

## Slide 10: Modeling for UQ
Interpretable predictions
Theoretically rigorous
Historically-proven legacy codes
Computationally intensive
Slow development & deployment
*Surrogate model, response surface, reduced-order model, kriging, metamodel, …….
Efficient predictions
Fast deployment
Widely available libraries
Lack interpretability (“Black Box”)
Ineffective for extrapolation/ sparse datasets
Machine Learning*
Data
Inputs
Outputs
Physics Simulation
Inputs
Outputs
Physics Simulation
Conservation laws
Boundary conditions
Physics-Based Modeling
Data-Driven Modeling
Constitutive Models
Notes: Strengths/weakness compliment eachother ;
ML fast deployment a double edged sword

## Slide 11: Outline: Machine Learning for UQ
Using machine learning surrogate models responsibly
Combining physics-based modeling & machine learning
  Multi-model Monte Carlo simulation
    Application: Trajectory simulation for entry, descent, and landing (EDL)
  Physics-informed generative adversarial networks (PI-GANs)
    Application: Material characterization for additive manufacturing
  Active learning with Gaussian Process models
    Application: Spacesuit reliability analysis
Summary

## Slide 12: Surrogate Modeling
Machine Learning
Gaussian processes
Neural networks
Polynomial Chaos
….
High-Fidelity
Model
Input
Training Data
Output
Training Data
…
Surrogate
Model
Offline
Online
…
Orders of magnitude computational speedup possible
Inputs
Outputs
from sklearn import <alg>
X,y = load_data()
mod = <alg>.fit(X, y)
y_new = mod.predict(X_new)
scikit-learn with Python:

## Slide 13: Surrogate Model Validation
…
…
…
…
Training
Testing
Training
Validation
High-Fidelity Model
Surrogate Model
Always create a separate dataset for testing that is not used for training
  Guards against the problem of overfitting
A third validation dataset is often used during training to tune machine learning hyperparameters (e.g., # layers, nodes in neural network)
If surrogate model error is non-negligible, it can be factored into total uncertainty when making probabilistic predictions
Hi-Fi Prediction
Surrogate Prediction
Notes: Analogous to calibrating a FEM model & validating on other test data

## Slide 14: Surrogate Modeling Pitfalls & Challenges
Not validating the effectiveness of surrogate prior to deployment
  Or validating the model using the training data!
Not accounting for (or correcting) surrogate errors when they are non-negligible
  Surrogate models yield biased estimators
Using surrogate model to extrapolate outside the range of training data
Training surrogate models from sparse training data
  Common when high-fidelity model is expensive to run
Notes: advanced ML approaches can address some of these challenges

## Slide 15: Combining Physics & Machine Learning (ML)
Fuse predictions from ML and physics-based models
Integrate physical laws into the training of ML models
Guide physics-based training data generation using ML Model
Multi-model Monte Carlo
Physics-informed deep learning
Active Learning
1. Multilevel Monte Carlo. Giles et al. 2015
2. Multifidelity Monte Carlo. Peherstorfer et al. 2016
3. Approximate Control Variates. Gorodetsky et al. 2019
4. Physics-informed neural networks. Raissi et al. 2019.
5. Physics-informed generative adversarial networks Yang et. al. 2018
6. Active learning in practice. Settles 2011.
7. Active learning for reliability analysis. Bichon et al. 2008.
Machine Learning
Data
Physics Equations
Outputs
Inputs
Machine Learning
Outputs
Inputs
Data
Physics Simulation
Physics Simulation
Machine Learning
Data
Outputs
Inputs
Application: Trajectory simulation for EDL
Application: Material characterization for additive manufacturing
Application: Spacesuit reliability analysis
Notes: Data-driven / physics-based synergy

## Slide 16: Combining Physics & Machine Learning (ML)
Fuse predictions from ML and physics-based models
Integrate physical laws into the training of ML models
Guide physics-based training data generation using ML Model
Multi-model Monte Carlo
Physics-informed deep learning
Active Learning
1. Multilevel Monte Carlo. Giles et al. 2015
2. Multifidelity Monte Carlo. Peherstorfer et al. 2016
3. Approximate Control Variates. Gorodetsky et al. 2019
4. Physics-informed neural networks. Raissi et al. 2019.
5. Physics-informed generative adversarial networks Yang et. al. 2018
6. Active learning in practice. Settles 2011.
7. Active learning for reliability analysis. Bichon et al. 2008.
Machine Learning
Data
Physics Equations
Outputs
Inputs
Machine Learning
Outputs
Inputs
Data
Physics Simulation
Physics Simulation
Machine Learning
Data
Outputs
Inputs
Application: Trajectory simulation for EDL
Application: Material characterization for additive manufacturing
Application: Spacesuit reliability analysis
Notes: Data-driven / physics-based synergy

## Slide 17: Multi-Model Monte Carlo (MC) for Trajectory Simulation
Motivation: high-precision guidance software for EDL
Challenge: enabling fast & accurate uncertainty propagation
  Using high-fidelity (Hi-Fi) trajectory simulations can be too slow
  Using low-fidelity (Lo-Fi) surrogate models lead to biased estimators
Approach: Combine predictions from a Hi-Fi model with Lo-Fi model(s) using multi-model MC to estimate trajectory state statistics
Atmosphere
Prob
Aerodynamics
Prob
Prob
Mass Properties
Trajectory Simulation Uncertainties
Hi-Fi Model
Predicted landing location
Low-Fidelity (Lo-Fi) Model
Low-Fidelity (Lo-Fi) Model
Lo-Fi Model
Collaborators: Anthony Williams (NASA), Som Dutta (NASA), Justin Green (NASA), Luke Morrill (NASA), Sam Nieomoeller (UCLA)

## Slide 18: Multi-Model Monte Carlo (MC) for Trajectory Simulation
Error versus Run Time for Expected Landing Location
High-fidelity MC requires the most run time for accurate estimators
Low-fidelity MC has irreducible error due to estimator bias
Multi-model MC is more efficient than high-fidelity MC & is unbiased
Example: predicting the expected landing location for an umbrella heatshield reentering the Earth’s atmosphere*
Models:
Hi-Fi: Program to Optimize Simulated Trajectories II (POST2)
Lo-Fi: Support vector machine (SVM) surrogate model
*J. E. Warner et al. Multi-Model Monte Carlo Estimators for Trajectory Simulation. AIAA SciTech. 2021.
Hi-Fi MC
Lo-Fi MC
Multi-Model MC

## Slide 19: Combining Physics & Machine Learning
Fuse predictions from ML and physics-based models
Integrate physical laws into the training of ML models
Guide physics-based training data generation using ML Model
Multi-model Monte Carlo
Physics-informed deep learning
Active Learning
1. Multilevel Monte Carlo. Giles et al. 2015
2. Multifidelity Monte Carlo. Peherstorfer et al. 2016
3. Approximate Control Variates. Gorodetsky et al. 2019
4. Physics-informed neural networks. Raissi et al. 2019.
5. Physics-informed generative adversarial networks Yang et. al. 2018
6. Active learning in practice. Settles 2011.
7. Active learning for reliability analysis. Bichon et al. 2008.
Machine Learning
Data
Physics Equations
Outputs
Inputs
Machine Learning
Outputs
Inputs
Data
Physics Simulation
Physics Simulation
Machine Learning
Data
Outputs
Inputs
Application: Trajectory simulation for EDL
Application: Material characterization for additive manufacturing
Application: Spacesuit reliability analysis
Notes: Data-driven / physics-based synergy

## Slide 20: Physics-Informed ML for Material Characterization
Motivation: Material characterization for additive manufacturing
Challenge: solving high-dimensional, probabilistic inverse problems
Approach: Implement physics-informed generative adversarial network (PIGAN) capable of estimating random material property fields from limited test data
  GANs: state-of-the-art deep neural networks to learn distributions from data
  Physics-informed: enables indirect estimation of material properties, use of smaller datasets
Collaborators: Julian Cuevas (U. Puerto Rico), Ted Lewitt (USC), Sean Lai (Portland State U.) – student interns at NASA

## Slide 21: Physics-Informed ML for Material Characterization
Example: Train PIGAN to generate samples of a lognormally-distributed, spatially-varying material stiffness using only deformation data*
  Synthetic DIC deformation data generated using the finite element method
*J. E. Warner et al. Inverse Estimation of Elastic Modulus Using Physics-Informed Adversarial Networks. NASA TM 2020-5001300. 2020.
Sensors
Problem Domain
Synthetic Deformation Data
Sample 1
Sample 2
X1 Def.
X2 Def.
Sample 1000
…
…
Solution Reference
Reference
PIGAN
Sample 1
Sample 2
Sample 3
Stiffness Samples
Stiffness Spatial Correlation
Stiffness Pointwise Probability Density

## Slide 22: Combining Physics & Machine Learning
Fuse predictions from ML and physics-based models
Integrate physical laws into the training of ML models
Guide physics-based training data generation using ML Model
Multi-model Monte Carlo
Physics-informed deep learning
Active Learning
1. Multilevel Monte Carlo. Giles et al. 2015
2. Multifidelity Monte Carlo. Peherstorfer et al. 2016
3. Approximate Control Variates. Gorodetsky et al. 2019
4. Physics-informed neural networks. Raissi et al. 2019.
5. Physics-informed generative adversarial networks Yang et. al. 2018
6. Active learning in practice. Settles 2011.
7. Active learning for reliability analysis. Bichon et al. 2008.
Machine Learning
Data
Physics Equations
Outputs
Inputs
Machine Learning
Outputs
Inputs
Data
Physics Simulation
Physics Simulation
Machine Learning
Data
Outputs
Inputs
Application: Trajectory simulation for EDL
Application: Material characterization for additive manufacturing
Application: Spacesuit reliability analysis
Notes: Data-driven / physics-based synergy

## Slide 23: Active Learning for Reliability Analysis
Motivation: reliability analysis of the xEMU spacesuit
Challenge: predicting small failure probabilities with expensive damage simulations
  Standard surrogate models are inaccurate for predicting extreme behavior (failure) with limited training data
Approach: use active learning to train Gaussian Process (GP) surrogate models that are tailored for accurate failure predictions
Collaborators: Robert Gramacy, Austin Cole, Annie Sauer (Virginia Tech)

## Slide 24: Active Learning for Reliability Analysis
Example: Estimate the probability of impact failure in the spacesuit under material/impact velocity uncertainty*
Compare surrogate-based solutions from:
  LHS GP – trained from random Latin Hypercube samples
  AL GP – trained using Active Learning targeting failure region
Hi-Fi LHS GP AL GP
2500 model evaluations
450 model evaluations
450 model evaluations
Probability of Failure Estimate Comparison
AL
LHS
* D. A. Cole et al. Entropy-Based Adaptive Design for Contour Finding and Estimating Reliability. Journal of Quality Technology. 2022.
Failure Threshold
Training Data Selection: LHS vs. ECL

## Slide 25: Summary
Trusting machine learning models for UQ:
  Use surrogate models responsibly:
    Always validate using a separate testing dataset
    Avoid extrapolation outside training data range
    Account for non-negligible surrogate errors in analysis
  Combine physics-based & data-driven approaches:
    Multi-model Monte Carlo: fuse predictions from ML with physics-based models for unbiased trajectory simulation estimators
    Physics-informed machine learning: integrate physical laws into the training of ML models for material characterization
    Active learning: guide physics-based training data generation using ML models for spacesuit reliability analysis

## Slide 26: References
Multi-model Monte Carlo
Physics-informed Deep Learning
Active Learning
Machine Learning
Data
Physics Equations
Outputs
Inputs
Machine Learning
Outputs
Inputs
Data
Physics Simulation
Physics Simulation
Machine Learning
Data
Outputs
Inputs
D. A. Cole, R. B. Gramacy, J. E. Warner, G. F. Bomarito, P. E. Leser, W. P. Leser. Entropy-Based Adaptive Design for Contour Finding and Estimating Reliability. Journal of Quality Technology. In Review (Preprint available). 2021.
B. K. Stanford, K. E. Jacobson, A. Sauer, J. E. Warner. Gradient-Enhanced Reliability Analysis of Transonic Aeroelastic Flutter. 2022 AIAA Scitech Proceedings.
J. E. Warner, J. Cuevas, P. E. Leser, G. F. Bomarito, W. P. Leser. Inverse Estimation of Elastic Modulus Using Physics-Informed Adversarial Networks. NASA TM 2020-5001300. May 2020.
J. E. Warner, G. F. Bomarito, L. Morrill, P. E. Leser, W. P. Leser, R. A. Williams, S. Dutta, S. Nieomoeller. Multi-Model Monte Carlo Estimators for Trajectory Simulation. 2021 AIAA SciTech Conference.
G. F. Bomarito, P. E. Leser, J. E. Warner, W. P. Leser. On the Optimization of Approximate Control Variates with Parametrically Defined Estimators. Journal Paper. Journal of Computational Physics. February 2022.
G. F. Bomarito, J. E. Warner, P. E. Leser, W. P. Leser, L. Morrill. Multi Model Monte Carlo with Python (MXMCPy). NASA TM 2020-220585. May 2020.
Email: james.e.warner@nasa.gov